## Slide 1
Towards HadronPhysics3

## Slide 2
JointGEM continuation
readout electronics
    n-XYTER ?
    T2K After ?
      active TPC
      large area prototype
              application
                homeland security ?
                medicine ?
FP7 – Call 8

## Slide 3: AFTER Main Features
Main features:
Input Current Polarity: positive or negative
72 Analog Channels
4 Gains: 120fC, 240fC, 360fC & 600fC
16 Peaking Time values: (100ns to 2µs)
511 analog memory cells / Channel:
Fwrite: 1MHz-50MHz; Fread: 20MHz
AFTER
511 cells
SCA
FILTER
100ns<tpeak<2us
CSA
1 channel
x72(76)
76 to 1
BUFFER
SCA MANAGER
SLOW CONTROL
Serial Interface
W / R
Mode
CK
CK
ADC
TEST
In Test
120fC<Cf<600fC
Power Supply
Reference Voltage
Reference Current
Asic Spy Mode
CSA;CR;SCAin (N°1)
Power
On
Reset
Slow Control
Power on reset
Test mode:
calibration or test [channel/channel]
functional [72 channels in one step]
Spy mode on channel 1:
CSA, CR or filter out
No zero suppress.
No auto triggering.
No selective readout.

## Slide 4: FAIR FEB-Developments (n-XYTER based)
FEB starter kit (Rafal Lalik) one-chip board for evaluative needs.
2chip FEB for gas detector readout  PANDA GEM-TPC
4chip FEB for Silicon detector readout, double sided
Flexcable as an alternative to PCBs: Studbonding of chips to micro cables
FEB starter kit board realized:
fully tested
manufacturing problems with fan-in make resubmission necessary  this Wednesday
employed FEB and SysCore2 to clarify interfacing issues
will use resubmission to fix a few minor bugs

## Slide 5
Hydrogen TPC
Neutron TPC
A detector that can identify neutrons and measure the direction that the neutrons arrived from could be useful for homeland security purposes.
The goal of the neutron TPC project (at LLNL) is to build such a detector from a hydrogen filled TPC.

## Slide 6
Hydrogen TPC
The detection principle is very simple. A fast neutron (~2MeV) from a fission source elastically scatters with the hydrogen in the TPC to produce a proton track in the gas. This proton is tracked and the direction of the proton is correlated with the direction of the incoming neutron. Although the kinematics of the scatter blurs the correlation, it only takes about 10 neutron scatters to reduce the cone of uncertainty to the neutron source down to about 16 degrees.

## Slide 7
A Highly multiplexed architecture to reduce the power consumption taking benefit of the low event rate
Read-out Electronic Architecture
Architecture principles
AFTER ASIC : 72 channels; Signal amplified & stored in the SCA (511 cells)
External trigger: digitization of the totality of the SCA of all the channels (2ms)
ADC + digital buffer mounted close to the detector
Multiple optical fibers send data to off-detector concentrators
Interface to common DAQ via standard network
Pre-amp and shapers
Samplers and multiplexers
Analog to digital conversion
Digital buffer
Data concentration
~124.000 channels
1728 AFTERs
On-detector electronics
72 Optical fibers
1-6 Tbaud*/s peak
*1 baud = 10 bit
~2 ms retention max.
34 Gbaud/s peak
400 Gbit/s peak
~1-10 Gbit/s averaged
Shared DAQ system
~0.1-1 Gbit/s
Standard LAN connection(s)
432 FEC
6 Concentrator Cards
72 Mezzanine cards
432 ADCs